## Slide 1
EE313: Wireless Communications
Professor WANG Rui
Department of Electronic & Electrical Engineering (EEE)
Southern University of Science & Technology (SUSTech)
Fall 2022

## Slide 2: This is a wireless world!

## Slide 3: Course Information
Course Materials:
  Blackboard System
Lectures:
  Tuesday 10:20-12:10 (3rd Teaching Building, Rm 206)
Instructor:
  Prof. WANG Rui (wangr@sustech.edu.cn)
TA:
  李乾任(12232135@mail.sustech.edu.cn)
  任振裕(renzy2022@mail.sustech.edu.cn)
  林铖(linc2022@mail.sustech.edu.cn)

## Slide 4: Course Information
Textbook:
  Andrea Goldsmith, Wireless Communications, Cambridge Press
Reference book:
  Theodore S. Rappaport, 无线通信原理与应用（第二版），电子工业出版社
Assessment:
  Theoretical part:
    Final exam
    Midterm exam
    Assignments & Quizzes
  Lab part:
    In-class hand-in
    After-class report

## Slide 5: Course Information
Goal:
  understand the fundamental principles underlying wire-less communications
Contents:
  characteristics and performance limits of wireless systems
  techniques of wireless communications
  mathematical tools to analyze the systems
  in-sights and trade-offs associated with system design
  the applications of the principles in current and envisioned wireless systems

## Slide 6: Course Syllabus
Overview of Wireless Communications
Path Loss, Shadowing, and Fading Models
Capacity of Wireless Channels
Digital Modulation and its Performance
Diversity
Coding
Adaptive Modulation
Equalization
MIMO Systems
Multicarrier Modulation
Spread Spectrum
Typical Wireless Systems

## Slide 7: Overview of Wireless Communications
Outline
  History of Wireless Communications
  Current and Emerging Wireless Systems
  Characteristics of Wireless Communications
  Technical Challenges

## Slide 8: The Amazing World of Wireless Communication Systems

## Slide 9: Early History of Wireless Communications
Many people in history used light for communication
  Flag signal
  Smoke signal (150 BC China, Greece)
    Set of signal combination convey messages
    Observation stations along the road act as relays
Telegraph and telephone replace the early comm. networks
  1838 Morse, 1876 Bell
Electromagnetic waves for modern wireless communications
  Faraday, Maxwell, Hertz

## Slide 10
120+ Year of Radio

## Slide 11: History of Wireless Communications
Many sophisticated military radio systems were developed during and after WW2
The first packet radio system:
  ALOHANET
  University of Hawaii 1971
Cellular has enjoyed exponential growth since 1988, with almost 5 billion users worldwide today
  Ignited the wireless revolution
  Voice, data, and multimedia ubiquitous
  Use in third world countries growing rapidly
Wi-Fi is enjoying tremendous success and growth
  Wide area networks (e.g. WiMax) and short-range systems other than Bluetooth (e.g. UWB) less successful

## Slide 12: Current and Emerging Wireless Systems
Cellular Systems
Wireless LANs
WiGig and mmWave
Satellite Systems
Bluetooth
Zigbee Radios
Sensor Networks
Biomedical Networks
Cognitive Radios

## Slide 13: Scarce Wireless Spectrum
Scarce and Expensive
$$$

## Slide 14: Value of Wireless Spectrum
2015年1月，美国联邦通信委员会（FCC）65MHz无线频谱拍卖获得449亿美元

## Slide 15: Spectrum Regulation
Spectrum is a scarce public resource
Spectrum allocation in US is controlled by FCC (commercial) or OSM (defense)
FCC auctions spectral blocks for set applications
Some spectrum set aside for universal use
Worldwide spectrum controlled by ITU-R

## Slide 16: Spectral Reuse
Due to its scarcity, spectrum is reused
BS
In licensed bands
Cellular
WiFi, BT, UWB,…
and unlicensed bands
Reuse introduces interference

## Slide 17: The Most Widely Deployed: Cellular Systems

## Slide 18: 1G, 2G, 3G, 4G

## Slide 19: 4G/LTE Cellular
Much higher data rates than 3G (50-100 Mbps)
  3G systems has 384 Kbps peak rates
Greater spectral efficiency (bits/s/Hz)
  Through MIMO, adaptive techniques
Flexible use of up to 100 MHz of spectrum
  20 MHz spectrum allocation common
Low packet latency (<5ms)
Reduced cost-per-bit
Support for multimedia
All IP network

## Slide 20: Wireless Local Area Network (WiFi)

## Slide 21: Wireless LAN Standards
802.11b (Old – 1990s)
  Standard for 2.4GHz ISM band (80 MHz)
  Direct sequence spread spectrum (DSSS)
  Speeds of 11 Mbps, approx. 500 ft range
802.11a/g (Middle Age– late 1990s-early 2000s)
  Standard for 5GHz band (300 MHz)/also 2.4GHz
  OFDM in 20 MHz with adaptive rate/codes
  Speeds of 54 Mbps, approx. 100-200 ft range
802.11n/802.11ac (around 2010 to now)
  Standard in 2.4 GHz and 5 GHz band
  Adaptive OFDM /MIMO in 20/40/80/160 MHz
  Antennas: 2-4, up to 8
  Speeds up to 600Mbps (> 1 Gbps), approx. 200 ft range
  Other advances in packetization, antenna use, etc.
Many
WLAN
cards
have
all 3
(a/b/g/n)
The latest:
WiFi 6

## Slide 22: WiGig
New standards operating in 60 GHz band
Data rates of 7-25 Gbps
Bandwidth of around 10 GHz (unregulated)
Range of around 10m (can be extended)
Uses/extends 802.11 MAC Layer
Applications include PC peripherals and displays for HDTVs, monitors & projectors

## Slide 23: mmWave
802.11ad & ay
  Couples 60GHz with massive MIMO and better MAC
  Promises long-range communication with Gbps data rates
  Hardware, propagation and system design challenges
  Much research on this topic today

## Slide 24: Why does WiFi Performance Sucks?
The WiFi standard lacks good mechanisms to mitigate interference, especially in dense AP deployments
  Multiple access protocol (CSMA/CD) from 1970s
  Static channel assignment, power levels, and carrier sensing thresholds
  In such deployments WiFi systems exhibit poor spectrum reuse and significant contention among APs and clients
  Result is low throughput and a poor user experience

## Slide 25: Satellite Systems
Cover very large areas
Different orbit heights
  GEOs (39000 Km) versus LEOs (2000 Km)
Optimized for one-way transmission
  Radio (XM, Sirius) and movie (SatTV, DVB/S) broadcasts
  Most two-way systems struggling or bankrupt
Global Positioning System (GPS) use growing
  Satellite signals used to pinpoint location
  Popular in cell phones, PDAs, and navigation devices

## Slide 26: Bluetooth/ Bluetooth Low Energy
Cable replacement RF technology (low cost)
Short range (10m, extendable to 100m)
2.4GHz band (crowded)
1 Data and 3 voice channels, up to 3Mbps
Widely supported by telecommunications, PC and consumer electronics companies
Keyboard, mouse, earphone, wrist strap, blood pressure monitor

## Slide 27: ZigBee Radios
Low-Rate WPAN
Data rates of 20, 40, 250 Kbps
Support for large mesh networking or star clusters
Support for low latency devices
CSMA-CA channel access
Very low power consumption
Frequency of operation in ISM bands
Focus is primarily on low power sensor networks

## Slide 28: Wireless Sensor Networks

## Slide 29: Example WSNs: Environmental Monitoring

## Slide 30: Example WSNs: Industrial and Agricultural Monitoring

## Slide 31: Applications in Health, Biomedicine and Neuroscience
Recovery from
Nerve Damage
Doctor-on-a-chip
Wireless
Network
Neuro/Bioscience
EKG signal reception/modeling
Brain information theory
Nerve network (re)configuration
Implants to monitor/generate signals
In-brain sensor networks
Body-Area
Networks

## Slide 32: Scarce Radio Spectrum
Spectrums has been sliced and allocated to existing users
Recent measurements show 70% allocated spectrums are not utilized
Unlicensed bands - biggest innovations in spectrum efficiency

## Slide 33: Cognitive Radio
Cognitive radio requirements
  Co-exists with legacy wireless systems
  Use their spectrum resources
  Does not interfere with them
Cognitive radio properties
  RF technology that “listens to” the usage of the spectrum
  Knowledge of primary users’ spectrum usage as a function of time and location
  Rules of sharing the available resources (time, freq, space)
  Intelligence to determine optimal transmission (bandwidth, time) based on primary user’s behavior

## Slide 34: Future Wireless Networks
Ubiquitous Communication Among People and Devices
Next-generation Cellular
Wireless Internet Access
Wireless Multimedia
Sensor Networks
Smart Homes/Spaces
Automated Highways
In-Body Networks
All this and more …

## Slide 35: Summary: What is Wireless Communications
Wireless Communication is the transfer of information between two or more points that are not connected by an electrical conductor
Information is transmitted using electromagnetic (EM) waves, also known as radio waves
For wireless services to be meaningful, we need
  Systems
  Devices
  Transmission and reception techniques
  Applications

## Slide 36: Wireless Systems are Segmented and Diverse
Segmented on applications, systems or coverage regions
  Applications: voice, Internet access, web browsing, paging, short messaging, video teleconferencing, sensing, distributed control…
  Systems: cellular, WLAN, satellite, ad hoc networks…
  Coverage region: personal, home, campus, city, regional, global
Diverse: different wireless applications have different requirements
  Wired networks can satisfy diverse requirements using a single protocol
  Wireless cannot! Fragmented in the near future!

## Slide 37: Difference compared with wired comm.
Channel varying
Movement
Open medium and high interference
Limited bandwidth
High BER
Limited resource and energy
Totally different design for various wireless systems

## Slide 38: Technical Challenges
Network Challenges
  Scarce spectrum
  Demanding/diverse applications
  Reliability
  Ubiquitous coverage
  Seamless indoor/outdoor operation
Device Challenges
  Size, Power, Cost
  Multiple Antennas in Silicon
  Multiradio Integration
  Coexistance
Cellular
Apps
Processor
BT
Media
Processor
GPS
WLAN
Wimax
DVB-H
FM/XM