## Slide 1
Wireless Communications
Members: 12011104 岳翼遥
12012128 孙逸涵
12011923 张旭东
Project: OFDM Technology
Date: 2022.12.14

## Slide 2
Introduction
01
CONTENTS
Theory
02
Basic Task
03
Advanced Task
04
Q&A
05

## Slide 3
Introduction
01
PART

## Slide 4
Introduction
EE313: Wireless Communications
4

## Slide 5
Introduction
EE313: Wireless Communications
5
How to deal with ISI ?
Approach 1: Increase the time interval to make it larger than the delay extension of multipath effect.
But it will reduce data transfer rate.
Approach 2: Channel equalizer.
Approach 3: Orthogonal Frequency Division Multiplexing (OFDM) is a digital multi‐carrier modulation technique extending the concept of single subcarrier modulation by using multiple sub-carriers over the channel.
Maximum delay
Complexity
Notes: As the maximum delay increases, the complexity of equalizers is correspondingly more and more complicated, which leads to the high computational complexity and unrealizable.
In particular, the number of taps required for an equalizer with good performance in a high–data-rate system is typically large. Thus, these equalizers are quite complex. Moreover, it is difficult to maintain accurate weights for a large number of equalizer taps in a rapidly varying channel.
Thus, most emerging high-rate wireless systems use multicarrier modulation

## Slide 6
Introduction
EE313: Wireless Communications
6
Advantages of OFDM technology
Spectra efficiency
Against frequency selective fading
The ISI can be completely eliminated through the use of a cyclic prefix
Use multi-subcarriers to decrease the complexity of equalizer
Application of OFDM technology
4G mobile communication system
Multi Input Multi Output (MIMO) technology
Ultra Wide Band (UWB) radios
IEEE 802.11a Wireless LAN
Digital Audio Broadcasting (DAB)
HiperLAN/2 (High Performance Radio LAN)
Notes: 中国的UWB标准采用了OFDM双载波技术,包含两个载波的OFDM超宽带信号进行数据传输
数字音频广播 (DAB)
HiperLAN是一种在欧洲应用的无线局域网通讯标准的一个子集

## Slide 7
Theory
02
PART
EE313: Wireless Communications
7

## Slide 8
Basic idea of OFDM
EE313: Wireless Communications
8
Think of the modulation symbol as the spectrum of the signal
IFFT at the transmitter
FFT at the receiver
Parallel transmission mode

## Slide 9
Basic idea of OFDM
EE313: Wireless Communications
9
Improve frequency band utilization rate

## Slide 10
Multipath Propagation
EE313: Wireless Communications
10

## Slide 11
Multipath Propagation
EE313: Wireless Communications
11
Frequency selective fading

## Slide 12
Multipath Propagation
EE313: Wireless Communications
12

## Slide 13
Multipath Propagation
EE313: Wireless Communications
13
Subchannel flat fading
subchannel overlap
Sample at zero crossing

## Slide 14
Adding Cycle Prefix
EE313: Wireless Communications
14

## Slide 15
Adding cycle prefix
EE313: Wireless Communications
15
N≥length(x[n])+length(h[n])-1

## Slide 16
Adding Cycle Prefix
EE313: Wireless Communications
16
M＞Delay extension of multipath propagation

## Slide 17
Insert None Tone
EE313: Wireless Communications
17
Insert 0 into the high-frequency component, which can avoid the transmission of high-frequency components.
Place the sequence at low frequency,easy to increase the length of the original sequence.

## Slide 18
OFDM Transmitter
EE313: Wireless Communications
18

## Slide 19
OFDM Transmitter
EE313: Wireless Communications
19
Convert serial input stream to parallel stream, size =N-K
Insert K null tones， size=N
Perform N IFFT
Add cycle prefix
Convert parallel stream to serial stream, size=N+Lc

## Slide 20
OFDM Receiver
EE313: Wireless Communications
20

## Slide 21
OFDM Receiver
EE313: Wireless Communications
21
Convert serial input stream to parallel stream, size = N+Lc
Remove cycle prefix， size=N
Perform N FFT
Apply frequency domain equalizier
Remove null tones，size =N-k
Convert parallel stream to serial stream

## Slide 22
Basic Task
03
PART
EE313: Wireless Communications
22

## Slide 23
Task1: Programming for OFDM Transceiver
EE313: Wireless Communications
23
OFDM
Transmitter
OFDM
Receiver

## Slide 24
Task2: Frequency Selectivity of Wireless Channels——Simulation
EE313: Wireless Communications
24
SampleRate=400KHz
SampleRate=800KHz
SampleRate=1MHz

## Slide 25
Task2: Frequency Selectivity of Wireless Channels——Simulation
EE313: Wireless Communications
25
SampleRate=2MHz
SampleRate=4MHz
SampleRate=5MHz

## Slide 26
Task2: Frequency Selectivity of Wireless Channels——USRP Experiment
EE313: Wireless Communications
26
SampleRate=400KHz
SampleRate=800KHz
SampleRate=1MHz

## Slide 27
Task2: Frequency Selectivity of Wireless Channels——USRP Experiment
EE313: Wireless Communications
27
SampleRate=2MHz
SampleRate=4MHz
SampleRate=5MHz

## Slide 28
Task3: Sensitivity to Frequency Offsets——Simulation
EE313: Wireless Communications
28
Frequency Offset=0Hz
Under [10 4 10 4] N=64
Frequency Offset=10Hz
Frequency Offset=20Hz

## Slide 29
Task3: Sensitivity to Frequency Offsets——Simulation
EE313: Wireless Communications
29
Frequency Offset=30Hz
Frequency Offset=200Hz
Under [10 4 10 4] N=64

## Slide 30
Task3: Sensitivity to Frequency Offsets——Simulation
EE313: Wireless Communications
30
Under [20 20 4 4] N=64
Frequency Offset=50Hz
Frequency Offset=100Hz
Frequency Offset=150Hz
Frequency Offset=200Hz
Frequency Offset=50Hz
Frequency Offset=100Hz
Frequency Offset=150Hz

## Slide 31
Task3: Sensitivity to Frequency Offsets——Simulation
EE313: Wireless Communications
31
Under [4 4 4 4] N=1024
Frequency Offset=50Hz
Frequency Offset=100Hz
Frequency Offset=150Hz

## Slide 32
Task3: Sensitivity to Frequency Offsets——Simulation
EE313: Wireless Communications
32
Under [20 20 4 4] N=1024
Frequency Offset=200Hz
Frequency Offset=150Hz
Frequency Offset=50Hz
Frequency Offset=100Hz

## Slide 33
Task3: Sensitivity to Frequency Offsets——Simulation
EE313: Wireless Communications
33
Under [10 4 10 4] N=512
Frequency Offset=50Hz
Frequency Offset=100Hz
Frequency Offset=150Hz

## Slide 34
Task3: Sensitivity to Frequency Offsets——Simulation
EE313: Wireless Communications
34
Under [10 4 10 4] N=1024
Frequency Offset=50Hz
Frequency Offset=100Hz
Frequency Offset=150Hz
As the number of subcarriers increases, the recovery quality becomes worse.

## Slide 35
Task3: Sensitivity to Frequency Offsets——USRP Experiment
EE313: Wireless Communications
35
Under [10 4 10 4] N=64
Frequency Offset=0Hz
Frequency Offset=10Hz
Frequency Offset=20Hz
Frequency Offset=30Hz

## Slide 36
Task3: Sensitivity to Frequency Offsets——USRP Experiment
EE313: Wireless Communications
36
Under [10 4 10 4] N=512
Frequency Offset=50Hz
Frequency Offset=100Hz
Frequency Offset=150Hz

## Slide 37
Task3: Sensitivity to Frequency Offsets——USRP Experiment
EE313: Wireless Communications
37
Under [10 4 10 4] N=1024
Frequency Offset=50Hz
Frequency Offset=100Hz
Frequency Offset=150Hz

## Slide 38
Task3: Sensitivity to Frequency Offsets——USRP Experiment
EE313: Wireless Communications
38
Problem
Under [10 4 10 4] N=512 50Hz
Capture time = 500u
Capture time = 4.8m

## Slide 39
Task3: Sensitivity to Frequency Offsets——USRP Experiment
EE313: Wireless Communications
39
Problem
Under [10 4 10 4] N=1024 50Hz
Capture time = 2.4m
Capture time = 4.8m

## Slide 40
Advanced Task
04
PART
EE313: Wireless Communications
40

## Slide 41
Advanced Task1 — High-order Modulation
EE313: Wireless Communications
41
16QAM Modulation
modulate_proj.vi

## Slide 42
Advanced Task1 — High-order Modulation
EE313: Wireless Communications
42
16QAM Demodulation
decode_proj.vi

## Slide 43
Advanced Task1 — 64QAM
EE313: Wireless Communications
43
64QAM Modulation

## Slide 44
Advanced Task1 — 64QAM
EE313: Wireless Communications
44
64QAM Demodulation

## Slide 45
Advanced Task1 — Simulator
EE313: Wireless Communications
45
16QAM
64QAM

## Slide 46
Advanced Task1 — USRP
EE313: Wireless Communications
46
16QAM
64QAM

## Slide 47
Advanced Task1 — Video
EE313: Wireless Communications
47
16QAM
64QAM

## Slide 48
Advanced Task2 — Image Transmission
EE313: Wireless Communications
48
Image source
Source(Image).vi

## Slide 49
Advanced Task2 — Image Transmission
EE313: Wireless Communications
49
Image recover

## Slide 50
Advanced Task2 — Simulator
EE313: Wireless Communications
50
Transmitted image
Recovered image

## Slide 51
Advanced Task2 — USRP
EE313: Wireless Communications
51
Image recover

## Slide 52
Advanced Task2 — Video
EE313: Wireless Communications
52
Image Transmission

## Slide 53
THANKS
EE313: Wireless Communications
53

## Slide 54
Q&A
EE313: Wireless Communications
54