## Slide 1: Lecture 1 Review
History of Wireless Comm.
Current and Emerging Wireless Systems
  Cellular, WiFi, Satellite, Bluetooth, Zigbee
  sensor network, biomedical network, cognitive radio
Characteristics of Wireless Comm.
Technical Challenges

## Slide 2: Lecture 2 Outline
Signal Propagation Overview
TX and RX Signal Models
  Complex baseband models
Path Loss Models
  Free-space Path Loss
  Ray Tracing Models
  Simplified Path Loss Model
  Empirical Models
Log Normal Shadowing
Combined Path Loss and Shadowing
Model Parameters from Measurements

## Slide 3: Recall what happens when EM wave encounters a new media
Reflection
Diffraction
Scattering
Absorption

## Slide 4: Reflection
Wave hits an object with dimension much larger than the radio wavelength will be partially reflected off the surface of the object

## Slide 5: Diffraction
Apparent bending of waves around small obstacles and the spreading out of waves past small openings

## Slide 6: Scattering
EM wave scattered by particles that are much smaller in diameter than the wavelength

## Slide 7: Absorption
The absorption of EM wave is often called attenuation
The energy of EM wave is taken up by some matter and transformed to other forms of energy, e.g., heat

## Slide 8: Propagation Characteristics
Path Loss (includes average shadowing)
Shadowing (due to obstructions)
Multipath Fading
Pr/Pt
d
Pr
Pt
d=vt
v
Very slow
Slow
Fast
large-scale
propagation effect
-- small-scale propagation effect

## Slide 9: Path Loss Modeling
Maxwell’s equations
  Complex and impractical
Free space path loss model
  Too simple
Ray tracing models
  Requires site-specific information
Simplified power falloff models
  Main characteristics: good for high-level analysis
Empirical Models
  Don’t always generalize to other environments

## Slide 10: Representation of Bandpass Signals
Bandpass signal:
  sI(t) is in-phase component, sQ(t) is quadrature component
Define a complex signal:
u(t) is called equivalent lowpass signal for s(t)

## Slide 11: Free Space (LOS) Model
Path loss and path gain:
  Path loss:
  Path gain:
Power falls off:
  Gl is the product of tx and rx antenna field radiation pattern in the LOS direction
  Proportional to 1/d2,l2
d

## Slide 14: Ray Tracing Approximation
Rx contains multipath signal components
Ray tracing:
  Assume a finite number of reflectors with known location and dielectric property
  Then, the received signal from each signal component can be calculated
  Typically includes reflected rays, can also include scattered and diffracted rays.
Accurate for rural area, city street and indoor environment

## Slide 15: Two Path Model
Path loss for one LOS path and one ground (or reflected) bounce
Delay spread: (x+x’-l)/c

## Slide 18: Two Path Model
Ground bounce approximately cancels LOS path above critical distance
Power falls off
  Proportional to d2 (small d)
  Proportional to d4 (d>dc)
  Independent of l (f)

## Slide 19: General Ray Tracing
Models all signal components
  Reflections
  Scattering
  Diffraction
Requires detailed geometry and dielectric properties of site
  Similar to Maxwell, but easier math.
Computer packages often used

## Slide 20: Simplified Path Loss Model
Used when path loss dominated by reflections.
Most important parameter is the path loss exponent g, determined empirically.
where is achieved from free-space model

## Slide 21: Indoor Propagation Model
Indoor model differ widely in the materials used for walls and floors, the layout of rooms, windows and obstructing objects
Difficult to find generic models
FAF: floor attenuation factor (8-20dB)
PAF: partition attenuation factor

## Slide 22: Empirical Channel Models
Cellular Models: Okumura model and extensions:
  Empirically based (site/freq specific)
  Awkward (uses graphs)
  Hata model: Analytical approximation to Okumura
  Cost 231 Model: extends Hata to higher freq. (2 GHz)
  Walfish/Bertoni: extends Cost 231 to include diffraction
WiFi channel models: TGn
  Empirical model for 802.11n developed within the IEEE standards committee. Free space loss up to a breakpoint, then slope of 3.5. Breakpoint is empirically-based.
Commonly used in cellular and WiFi system simulations

## Slide 23: Shadowing
Models attenuation from obstructions
Random due to random # and type of obstructions
Typically follows a log-normal distribution
  dB value of power is normally distributed
  m=0 (mean captured in path loss), 4 dB<s<13 dB (empirical)
  Central limit theorem can be used to explain this model

## Slide 25: Combined Path Loss and Shadowing
Linear Model: y lognormal
dB Model
Pr/Pt
(dB)
log d
Very slow
Slow
10logK
-10g

## Slide 26: Outage Probability
Path loss: circular cells
Path loss + shadowing: amoeba cells
  Tradeoff between coverage and interference
Outage probability
  Probability received power below given minimum

## Slide 28: Cell Coverage Area
Cell coverage area
  % of cell locations at desired power
  Increases as shadowing variance decreases
  Large % indicates interference to other cells

## Slide 29: Main Points
Path loss models simplify Maxwell’s equations
Models vary in complexity and accuracy
Power falloff with distance is proportional to d2 in free space, d4 in two path model
Main characteristics of path loss captured in simple model Pr=PtK[d0/d]g
Empirical models used in simulations
  Low accuracy (15-20 dB std)
  Capture phenomena missing from formulas
  Can be awkward to use in analysis

## Slide 30: Main Points
Random attenuation due to shadowing modeled as log-normal (empirical parameters)
Combined path loss and shadowing leads to outage and amoeba-like cell shapes
Cellular coverage area dictates the percentage of locations within a cell that are not in outage

## Slide 31: Assignment
Read Chapter 2
Homework: 2-2, 2-13, 2-17, 2-19