## Slide 1: Lecture 3
Statistical Multipath Channel Models
(Small-Scale Fading)

## Slide 2: Review of Lecture 2
Path loss models simplify Maxwell’s equations
Models vary in complexity and accuracy
Power falloff with distance is proportional to d2 in free space, d4 in two path model
Main characteristics of path loss captured in simple model Pr=PtK[d0/d]g
Empirical models used in simulations
  Low accuracy (15-20 dB std)
  Capture phenomena missing from formulas
  Can be awkward to use in analysis

## Slide 3: Review of Lecture 2
Random attenuation due to shadowing modeled as log-normal (empirical parameters)
Combined path loss and shadowing leads to outage and amoeba-like cell shapes
Cellular coverage area dictates the percentage of locations within a cell that are not in outage

## Slide 4: Recall the Propagation Effect
Path Loss (includes average shadowing)
Shadowing (due to obstructions)
Multipath Fading
Pr/Pt
d
Pr
Pt
d=vt
v
Very slow
Slow
Fast
large-scale
propagation effect
-- small-scale propagation effect

## Slide 5: Lecture 3 Outline
Time Varying Channel Impulse Response
Narrowband Fading Model
Flat Fading vs. Frequency Selective Fading
Effect of Flat and Frequency Selective Fading
Signal Envelope Distributions (Rayleigh and Rician)
Average Fade Duration

## Slide 6: Lecture 3 Outline
Time Varying Nature of Channel Fading
Scattering Function
Multipath Intensity Profile
Doppler Power Spectrum

## Slide 7: Multipath Fading
Results from
  Interference between multiple paths with different path lengths
  Movement of the mobile or environment makes this effect time varying
  Rate of variation of the channel characteristics is measured by Doppler Frequency

## Slide 8: Multipath Fading
Random # of multipath components, each with
  Random amplitude
  Random phase
  Random Doppler shift
  Random delay
Random components change with time
Leads to time-varying channel impulse response

## Slide 9: Physics of Multipath Fading

## Slide 10: Review of Impulse Response of a Linear System

## Slide 11: Example

## Slide 12: Time-Varying Linear System

## Slide 13: Time-Varying Multipath Channel

## Slide 14: Time Varying Impulse Response
Response of channel at time t to impulse input at time t-t:
  : impulse response of the channel at time t to the impulse input at time t-t
  : random amplitude
  : random phase
  : random delay

## Slide 17: Received Signal Characteristics
Received signal consists of many multipath components
Amplitudes change slowly
Phases change rapidly
  Constructive and destructive addition of signal components
  Amplitude fading of received signal (both wideband and narrowband signals)

## Slide 18: Narrowband Model
Assume delay spread maxm,n|tn(t)-tm(t)|<<1/B
Then u(t)u(t-t).
Received signal given by
No signal distortion (spreading in time)
Multipath affects complex scale factor in brackets.

## Slide 20: Wideband Channels
Individual multipath components resolvable
True when time difference between components exceeds signal bandwidth
t
t
Narrowband
Wideband

## Slide 21: Flat Fading vs. Frequency Selective Fading
Flat fading:
  N(t)=1, i.e. no delay spread
  Channel impulse response is one single impulse
  The frequency response is a constant (over the communication bandwidth)
  Usually occurs for narrowband communication, i.e., low symbol rates

## Slide 22: Flat Fading vs. Frequency Selective Fading
Frequency selective fading:
  N(t)>1 i.e. with delay spread
  Channel impulse response consists of multiple impulses
  The frequency response varies over the communication bandwidth
  Usually occurs for wideband communication, i.e., high symbol rates

## Slide 23: Effect of Flat Fading
Flatten BER curves
Around 15dB penalty when BER is 10-3

## Slide 24: Effect of Frequency Selective Fading
Multipath  Inter-symbol interference (ISI)
Result in irreducible error floor

## Slide 25: Signal Envelope Distribution for Narrow Band Model
CLT approx. leads to Rayleigh distribution (power is exponential)
When LOS component present, Ricean distribution is used
Measurements support Nakagami distribution in some environments
  Similar to Ricean, but models “worse than Rayleigh”
  Lends itself better to closed form BER expressions

## Slide 26: Rayleigh Channel

## Slide 27: Rician Channel
LOS channels：

## Slide 28: Level Crossing Rate and Average Fade Duration
LCR: rate at which the signal crosses a fade value Z in the downward direction
  where
AFD: How long a signal stays below target Z
  Derived from LCR
For Rayleigh fading
  Depends on ratio of target to average level (r)
  Inversely proportional to Doppler frequency
Z
t1
t2
t3

## Slide 29: Main Points
Time Varying Channel Impulse Response
Narrowband Fading Model
Flat Fading vs. Frequency Selective Fading
Effect of Flat and Frequency Selective Fading
Signal Envelope Distributions (Rayleigh and Rician)
Average Fade Duration

## Slide 30: Time Varying Nature of Wireless Channel
Cause for time-varying nature
  movements of mobile or objects in the environment
On each path, is a random process
This random process is correlated in time
The faster the autocorrelation function decays with the time difference, the faster the channel varies
To measure how fast the channel varies: Doppler spread and coherence time.

## Slide 31: Doppler Shift
Doppler frequency shift
Doppler spread: the maximum Doppler shift

## Slide 32: Doppler Shift

## Slide 33: Assignment
Read Chapter 3
Homework: 3-3, 3-6,3-8,3-12

## Slide 34: Review of Last Lecture
Time Varying Channel Impulse Response
Narrowband Fading Model
Flat Fading vs. Frequency Selective Fading
Effect of Flat and Frequency Selective Fading
Signal Envelope Distributions (Rayleigh and Rician)
Average Fade Duration
Time Varying Nature of Channel Fading

## Slide 35: Autocorrelation Function
Channel impulse response is a random process
is a complex Gaussian process, is characterized by mean, autocorrelation and cross correlation.
Autocorrelation:
Mean = 0, crosscorrelation = 0

## Slide 36: Scattering Function
Wide sense stationary:
Uncorrelated scattering
Scattering function is Fourier trans. of Ac(t,Dt):
(with respect to Dt)
t:
r:
multipath delay function
Doppler frequency

## Slide 37: Scatter Function
Scattering function is the average output power of the channel as a function of τ,
r

## Slide 38: Power Delay Profile
Power Delay Profile (multipath intensity profile)
  Let Dt=0 in Ac(t, Dt), written as Ac(t)
  Average power associated with a given multipath delay
  Determines average and rms delay spread
Coherence Bandwidth
Signals separated in frequency by Bc is uncorrelated

## Slide 39: Doppler Power Spectrum
Doppler Power Spectrum
  Let Df =0 in AC(Df , Dt) AC(Dt)
  DPS: Fourier Trans. of AC(Dt) with respective of Dt
  Determines Doppler spread: Bd is maximum doppler r for which Sc (r)=>0
Coherence Time: Tc=1/Bd
  Signals separated in time by Tc is uncorrelated
2Tc
2Bd
captial C

## Slide 40: Summary
Ac(τ): Power delay profile
∆t=0
∆f=0
Sc(r): Doppler power spectrum
BD: Doppler spread
∆t=0
∆f=0

## Slide 41: Summary

## Slide 42: Main Points
Scattering Function
Power Delay Profile  Coherence Bandwidth
Doppler Power Spectrum  Coherence Time
Flat/Frequency Selective Fading
Fast/Slow Fading